## Slide 1
Real-Time Data Acquisition
and Processing for High-Resolution
Synchrotron Micro-Tomography
Anas Mohammad*
Experimental Data Engineer
Data Collection & Analysis Team @SESAME
Mustafa Alzubi Team Leader

## Slide 2
SESAME Synchrotron | Data Collection & Analysis| 2026
Overview
Challenge: BEATS beamline generates up to 2TB daily at speeds reaching several GB/s
Problem: Time gap between receiving camera frames and writing them to storage
Solution: Developed BEATSH5Writer with circular buffer indexing in C++ for real-time performance
Result: Real-time data writing with zero frame losses at maximum camera throughput

## Slide 3
BEATS Beamline Overview
2560×2160
Resolution
100 FPS
Frame Rate
1.14 GB/s
Throughput
2 TB/day
Data Volume
Capabilities
Non-destructive 3D imaging (SRCT)
High-resolution microscopic imaging
Thousands of projections per scan
3D volumetric reconstruction
Infrastructure
PCO edge 5.5 / FLIR Oryx cameras
CPU/GPU reconstruction cluster
0.5 PB GPFS + tape archival
100 Gbps InfiniBand network
Challenge: Time gap between receiving frames and writing to storage grows with dataset size
SESAME Synchrotron | Data Collection & Analysis| 2026

## Slide 5
System Architecture
Key Design Principles
✓
Direct streaming to storage - no local buffering at beamline
✓
Real-time ZeroMQ data transmission over 100 Gbps InfiniBand
✓
HDF5-DXfile format standard for tomography data
SESAME Synchrotron | Data Collection & Analysis| 2026

## Slide 6
The Problem: Growing Time Gap
Writer Performance - Python Implementation
Chart: 
| 500 | 1000 | 1500 | 2000 | 2500 | 3000
Receive Time | 6.73 | 10.4 | 15 | 20 | 25 | 23.15
#REF! | 1
Enhanced Python | 10.4 | 20.8 | 31.89 | 60.07 | 70 | 80
Limitation
Still 3.5× slower
than receive time
Queue bottleneck
remains
SESAME Synchrotron | Data Collection & Analysis| 2026
Root Causes
Dequeuing from FIFO queue
1D → 2D array reshaping
CPU-intensive operations
Queue size degradation

## Slide 7
Memory Management Challenge
Why Memory Became the Bottleneck
Initial System (96 GB RAM)
Max: ~8,000 frames (88.4 GB)
Queue grows with frame count
Access time degrades
Insufficient for large scans
Upgraded System (192 GB RAM)
Max: ~17,000 frames (188 GB)
Supports worst-case: 14,000 frames
Buffer headroom for processing
Ready for optimization attempts
Frame Data in Memory
1D Array from Camera
5,697,500 pixels × 16-bit = 11.4 MB per frame
Reshaping Required: 1D → 2D (2560 × 2160)
SESAME Synchrotron | Data Collection & Analysis| 2026

## Slide 8
Our Solution Journey
1
RAM Upgrade
96 GB → 192 GB
Baseline capacity
2
Python Parallel
4 workers + static hashing
~4× improvement
3
Shared Memory
Direct memory access
Failed at 6K frames
4
C++ Ring Buffer
Smart pointers + HDF5 API
Real-time success! ✓
SESAME Synchrotron | Data Collection & Analysis| 2026

## Slide 9
C++ Ring Buffer Implementation
std::vector<std::unique_ptr<std::pair<std::string, std::vector<size_t>>>>
Ring Buffer Structure
Key Advantages
std::vector for dynamic sizing
reserve() pre-allocates memory
Smart pointers prevent memory leaks
std::unique_ptr ensures ownership
std::move semantic
std::pair handles JSON metadata
size_t for dynamic frame sizes
SESAME Synchrotron | Data Collection & Analysis| 2026

## Slide 10
Final Performance Achievement
C++ Ring Buffer: All Implementations Compared
Chart: 
| 500 | 1000 | 1500 | 2000 | 2500 | 3000
Receive Time | 6.73 | 10.4 | 15 | 20 | 25 | 23.15
#REF! | 1
Python Performance | 10.4 | 20.8 | 31.89 | 60.07 | 70 | 80
C++ Performance | 6.9 | 10.4 | 15 | 20.8 | 25 | 36.7
@ 3000 Frames
C++ Time:
36.7s
Receive:
23.2s
Difference:
13.5s
Performance Gains
70% faster
than original
Near real-time:
Write ≈ Receive
SESAME Synchrotron | Data Collection & Analysis| 2026

## Slide 11
Production Deployment Results
Stress Test
20 consecutive experiments
15,000 frames each @ 100 FPS
Maximum resolution (2560×2160)
3.1 TB total data
Results
✓ Zero frame losses
✓ Sustained 1.14 GB/s I/O
✓ No cached data
✓ 100% success rate
584
Experiments
In production
23.8 TB
Data Collected
Successfully
100%
Reliability
Zero failures
0
Frame Losses
Perfect capture
SESAME Synchrotron | Data Collection & Analysis| 2026

## Slide 12
Impact & Contributions
Technical Innovation
Ring buffer with smart pointers for memory management
Identified queue access as bottleneck in high-throughput pipelines
Software-based solution without specialized hardware
Scientific Impact
Immediate data availability accelerates research
Enables demanding high-throughput experiments
Template for other synchrotron facilities worldwide
Documented open-source solution on GitHub
Contribution
This work has been submitted in IEEE Transaction
SESAME Synchrotron | Data Collection & Analysis| 2026

## Slide 13
Thank You
Questions & Discussion